DATE:

PROPOSAL FOR OUR MODEL:

3300-CTA Conveyorized Automatic

NOTE:  Photo shows Model 3300-CTA1 “Center Section Only”

Cousins Packaging Inc.          105 Claireport Crescent          Etobicoke, Ontario, Canada M9W 6P7

1-888-209-4344 or 416-743-1341         fax 416-743-1831

www.cousinspackaging.com

## MODEL 3300-CTA  HEAVY DUTY CONVEYORIZED

AUTOMATIC STRETCH WRAP SYSTEM

GENERAL SPECIFICATIONS

PRODUCTION SPEED:

- 1-40 loads per hour

NOTE: Process rates will vary with load size, number of wraps & forklift load/unload time

LOAD CAPACITY:

- Maximum load weight:	4,000# dynamic – 12,000# static

- Maximum load size:		48” W x 48” L (68” max. load diagonal) x 75” H (+ up to 4” top overlap)

- Minimum load size:		30” W x 30” L x 24” H

TURNTABLE:

- 72” diameter 3/8” thick laser-cut steel plate with 5” skirt

- Front and side cut-outs with UHMW flexible contouring for fork truck access

- 6-point heavy duty ball bearing caster support system

- ANSI # 60 direct chain drive c/w chain tensioner

- 3-16 RPM rotational speed c/w soft start acceleration

- 3/4 HP AC variable speed motor c/w turntable holding brake

- Final revolution deceleration and positive stop alignment

FILM CARRIAGE ELEVATOR:

- 1/2 HP AC variable speed motor

- ANSI #40 direct chain drive c/w shock dampener & Anti-Fall Safety Device

- Maintenance free carriage guidance system

FILM DELIVERY SYSTEM:

- NEW Super Rapid Thread II™ 20” capacity pre-stretch film carriage

- Special Film Threading Device – Uniquely orientates the sticky side of the film against the pre-stretch rollers and the inside of the load.

- 1/2 HP AC variable speed motor

- Fully electronic dynamic dancer corner compensation

- 33% to 313% fixed stretch capability

- Pre-stretch ratio variable using easy sprocket change

- Carriage Descent Obstruction Safety Shut-Off Device

- Rapid Thread ™ Safety Door with auto power cut-off switch

- Side mounted film carriage for operator convenience and safety

- Superior film-to-roller contact area

- Lifetime warranty on pre-stretch rollers

POWERED ROLLER CONVEYOR:

Standard turntable and optional infeed/outfeed sections:

- Chain driven live roller conveyor rated 4,000# per section

- 2-1/2” diameter 11 gauge rollers c/w 11/16” hex axles on 3” centers

- ANSI # 40 roller to roller chain drive

- 50” effective roller width

POWERED ROLLER CONVEYOR…continued…:

- Conveyor speed variable up to 30 FPM with electronic soft start

- Pass-line height – 16-1/2” from floor to top of rollers

- 1/2 HP AC variable speed motor

CONTROL FEATURES:

- PANASONIC PLC with Touchscreen Operator Interface

- Power Off – On – Reset switch & Power On indicator light

- Cycle Pause for applying top sheets

- Reinforce Wrap control for mid-wrapping

- Emergency Stop button

- Turntable Jog button

- Film Carriage Lower & Raise buttons

- Eject Load (Turntable Conveyor Jog) button

- Film tension (Force-to-Load) control

- Selectable Reduced Bottom Film Force parameter for wrapping bottom of load

- Separate film carriage raise & lower speed controls

- Variable turntable speed control

- Triple beam automatic load height sensing photo-eye, detects dark or shiny loads

- Separate 1 to 12 revolution top & bottom wrap control

- Gravity conveyor full photo-eye

- Broken film/out of film detection c/w automatic machine reset

- Beacon light indicates run, clear or fault conditions

- Wireless remote start/stop control – optional lanyard, pendant or pedestal control station available

- NEMA 12 control panel enclosure

- Non-proprietary UL/CSA approved components

AUTOMATION FEATURES:

- Pneumatically actuated film clamp mechanism

- Electro-mechanically actuated film tail cut/wiper arm mechanism

- Ni-chrome impulse hot wire film cut off c/w automatic periodic cleaning cycle

STRUCTURAL FEATURES:

- All structural steel construction

- Forklift truck portable base structure design – lifting tubes included for front and rear access

- Structural steel tube machine tower with sheet metal covers

- Electro-static powder coated paint finish

ELECTRICAL INPUT REQUIREMENT:

- 115 Volts 1 Phase 60 Hz 20 Amps

All the programming options

can be easily accessed by the

Panasonic Touchscreen

Operator Interface

PNEUMATIC REQUIREMENT:

- 3 CFM @ 80 PSI clean dry pneumatic supply required

- Filter/regulator c/w gauge & lock-out valve provided

Performance Inspired Super Rapid Thread II film carriage standard with the 3300-CTA

The Super Rapid Thread ll film carriage is patent pending and is

the most innovative carriage design to date.  In the past, most

manufacturers decided to use easy thread safety doors for the

ease of film threading and safety.  This reduced the “film-to-pre-

stretch roller” contact area as indicated in figure 1 (Industry

Winding Pattern With Safety Door).  In addition to this, the idler

rollers on the doors often fell out of alignment.  These two

issues increased what the industry refers to as film slippage.

People didn’t pay much attention to this in the past, though it

could add up to thousands of dollars, often doubling film

usage.  Due to the increasing cost of stretch film, people started

paying a lot more attention to their pre-stretch values and were

astonished to discover huge differences.

This is the inspiration for the Super Rapid Thread ll.

The Super Rapid Thread II has:

- The largest film to pre-stretch roller contact area of any machine on the market

- Only one floating nip roller on the access door that automatically aligns every time you close the door

- 2 nip/idler rollers are rigidly fixed (cannot move)

- No spring-loaded nip rollers

- Patent pending threading device for ease of threading

- One of the few carriages on the market that correctly puts the sticky side of the film against both the pre-stretch rollers and the inside of the load

- Safety electrical interlock – shuts the power off when the carriage access door is open

- Carriage anti-fall device.  If the chain breaks the carriage can’t fall

- Carriage descent obstruction plate.  Stops the film carriage descent if an obstacle is detected

The film carriage is the most critical device on the machine.

The SUPER RAPID THREAD II requires no tuning!!

Select the model below that best fits your requirements.

OFF-LINE:	Installed as a stand-alone system with the loads being brought to and from

the system by forklifts.  Cycle start is initiated by the operator.

IN-LINE: 	Installed in-line with conveyors or equipment provided by others.  Cycle start is initiated by a signal sent to the 3300-CTA control panel from another source.

Since this system starts automatically, the safety fencing option is required

| MODEL | DESCRIPTION | BASE PRICE |
| --- | --- | --- |
| 3300-CTA | Powered Turntable Conveyor with 5’ Gravity Outfeed | $ 23,990 |
| OFF-LINE | SEQUENCE OF OPERATION: Pallet is positioned on the turntable by forklift, operator initiates cycle start from the forklift using the standard pushbutton pendant, wrapped load is automatically conveyed to the non-powered gravity outfeed section so that the turntable is clear and ready to accept the next load. IMPORTANT! The basic 3300-CTA cannot be installed in-line with conveyors supplied by others. It does not have the necessary infeed transition rollers or logic. |  |
| 3300-CTA1 | Powered Turntable – Center Section Only | $ 25,900 |
| OFF-LINE | SEQUENCE OF OPERATION FOR: Pallet is conveyed to the turntable by conveyors provided by others and starts wrap cycle, wrapped load is automatically conveyed to the outfeed conveyor provided by others so that the turntable is clear and ready to accept the next load. NOTE: For in-line operation add the “In-Line Automation Package” option |  |
| 3300-CTA2 | Powered Turntable Conveyor with 5’ Powered Infeed & 5’ Gravity Outfeed | $ 29,480 |
| OFF-LINE | SEQUENCE OF OPERATION FOR: Pallet is positioned on the infeed conveyor by forklift, operator initiates cycle start from the forklift using the standard pushbutton pendant, load is conveyed to the turntable and starts wrap cycle, wrapped load is automatically conveyed to the non-powered gravity outfeed section so that the turntable is clear and ready to accept the next load. NOTE: For in-line operation add the “In-Line Automation Package” option |  |
| 3300-CTA3 | Powered Turntable with 5’ Powered Infeed & 5’ Powered Outfeed Conveyors | $ 34,030 |
| OFF-LINE | SEQUENCE OF OPERATION FOR: Pallet is positioned on the infeed conveyor by forklift, operator initiates cycle start from the forklift using the standard pushbutton pendant, load is conveyed to the turntable and starts wrap cycle, wrapped load is automatically conveyed to the powered outfeed section so that the turntable is clear and ready to accept the next load. NOTE: For in-line operation add the “In-Line Automation Package” option |  |

PRICING SUMMARY:

SELECTED MODEL:

| INSERT SELECTED MODEL NUMBER: | 3300- | INSERT BASE PRICE: |  |
| --- | --- | --- | --- |

REQUESTED OPTIONS:

|  | None Requested |  |
| --- | --- | --- |

| TOTAL SYSTEM PRICE INCLUDING REQUESTED OPTIONS: |  |
| --- | --- |

ADDITIONAL AVAILABLE OPTIONS FOR YOUR CONSIDERATION:

| A | OILA-PKG – In-line Automation Package – modified to be in-line with conveyors provided by others – includes interface relays and the safety fencing option (option E below) | $ 3,220 |
| --- | --- | --- |
| B | OSSPK – Starter spare parts kit | $ 1,450 |
| C | OEWH-110-S – Tower extension for 110” wrap height capability (standard is 75”) (this option includes a 5” tower pedestal – required to allow tower knock-down for shipment) NOTE: All machines with tower extensions will be hinged and shipped knocked-down | $ 995 |
| D | OTWRPED5 – 5” Tower Pedestal for HP models - adds 5” wrap height | $ 150 |
| E | OSFPKG-33 – Safety fence package with Interlocked Safety Gate (48" high open rail barrier type fence) (required for in-line systems) | $ 2,200 |
| F | OLNYRD-S – Lanyard pull switch in place of standard wireless remote (mounts to ceiling) | $ 250 |
|  | OPCS - Start/stop pendant station with 40’ cord in place of wireless remote | $ 250 |
| H | OPED-SS – Pedestal Start/Stop station in place of wireless remote | $ 325 |
| I | OWRC-ARC – Additional transmitter for the wireless remote start/stop control (one included with the machine) | $ 95 |
| J | ONSV208Y120 – Non-standard voltage 208Y/120 Volts 3 phase 60 Hz | $ 500 |
| K | ONSV230-3 – Non-standard voltage 230V or 460V 3 phase (specify voltage) | $ 1,350 |
| L | OABMLX1K4 – Allen-Bradley MicroLogix 1400 PLC in place of standard Panasonic FP-X | $ 1,700 |
| M | OFTSPE – Load/unload forklift safety photo-eye and logic (specify load or unload position) | $ 680 |
| N | O33CDLRCVR – Any additional 5’ powered infeed or outfeed conveyor section, per section. This option may require a non-standard voltage option for increased electrical demand | $ 4,550 |
| O | ONGC – Delete standard 5’ gravity outfeed conveyor if not required NOTE: Contour transition rollers & outfeed full photo-eye are retained | ($ 450) |

Notes:

- Installation by others

- Factory start-up tech available @ $ 750.00 day plus expenses - billed separately – allow minimum two days.

STANDARD TERMS AND CONDITIONS

TERMS:

- 1/3 down payment with order, 1/3 prior to shipment, balance net 30 days after shipment on approved credit (OAC) - receiving company federal ID#, contact name & phone number required with order.

These terms may change at the discretion of our accounting department.

TAXES:

- Applicable taxes not included.

FOB POINT:

- Factory – Toronto, Ontario (Canada). Freight prepaid and added to invoice.

SHIPMENT:

- Approximately 8 - 10 weeks from receipt of order and down payment (and approved drawings if applicable). Addition of options may add to lead-time.

This lead-time is based on current production conditions and can change without notification.

START-UP SUPERVISION:

- Start-up supervision is highly recommended for in-line conveyorized automatic systems such as the 4100-45-OHA, 6100-CTA & 7100-OHA, and is available for $750 per day plus expenses.  Two days on-site are typically sufficient.  Weekend start-ups will incur extra charges.

WARRANTY:

- Lifetime on blue pre-stretch rollers, 5 years on metal fabrications and 3 years on buyout components. (see below).

PRICE PROTECTION:

- All prices are valid for thirty (30) days from date of quotation.

STANDARD MACHINE WARRANTY

Effective May, 2011

All components used in the manufacture of pallet wrap equipment and associated parts by Cousins Packaging are warranted to be free from defects in material and workmanship for a period from date of shipment as follows: lifetime on blue pre-stretch rollers, five (5) years for metal fabrications manufactured by Cousins Packaging and three (3) years for buyout components (items purchased by Cousins).  Cousins Packaging will, at its sole discretion, repair or replace any defective components.

Not covered by this warranty is normal wear of components such as, but not limited to; belts, chains, fuses, bulbs, etc., or misuse or abuse of the machine or any components thereof.  As well, parts returned without the prescribed paperwork will not be covered by this warranty.  Labor to remove or repair any component is also not covered by this warranty.  Damage in transport is the responsibility of the carrier and is not covered under our warranty.

Except as stated herein, Cousins Packaging makes no other warranty, expressed or implied, nor does it assume or authorize anyone else to assume for it, any other obligation relating to Cousins’ machinery or equipment.  This warranty does not apply to equipment that, in the opinion of Cousins Packaging, has been subjected to misuse, neglect, or has been repaired or altered by unauthorized personnel.  All defective parts must be returned in their original state.  Defective parts that have been disassembled or damaged during removal or otherwise tampered with will not be covered under warranty, unless otherwise stated in writing by Cousins Packaging.  Cousins Packaging makes no warranty as to fitness of equipment for particular purposes.  Cousins Packaging Inc.’s sole obligation under this warranty will be to provide for repairs to components or replacement of parts, FOB Cousins Packaging Inc., Etobicoke, Ontario, Canada.